## Slide 1: Troubleshooting

## Slide 3
40 miljoen kinderen vaccinaties…

## Slide 9
Error Cost Escalation Through the Project Life Cycle - NASA

## Slide 10
Error Cost Escalation Through the Project Life Cycle - NASA

## Slide 13
Da Havilland Comet
Three fatal Comet 1 crashes due to structural problems, specifically BOAC Flight 783 on 2 May 1953, BOAC Flight 781 on 10 January 1954, and South African Airways Flight 201 on 8 April 1954, led to the grounding of the entire Comet fleet. After design modifications were implemented, Comet services resumed in 1958.[82]
Although commercial sales for the design never fully recovered, the redesigned Comet Mark 2, Mark 3 and Mark 4 series designs enjoyed a productive career of over the next 30 years.

## Slide 14
However, within a year of entering airline service, problems started to emerge, with three Comets lost within twelve months in highly publicised accidents, after suffering catastrophic in-flight break-ups. Two of these were found to be caused by structural failure resulting from metal fatigue in the airframe, a phenomenon not fully understood at the time. The other one was due to overstressing of the airframe during flight through severe weather. The Comet was withdrawn from service and extensively tested. Design and construction flaws, including improper riveting and dangerous concentrations of stress around some of the square windows, were ultimately identified. As a result, the Comet was extensively redesigned, with oval windows, structural reinforcements and other changes. Rival manufacturers meanwhile heeded the lessons learned from the Comet while developing their own aircraft.

## Slide 15: Troubleshooting
Brainstorming
Isoleren
(waar zit het?)
Segmenteren
(onder welke omstandigheden?)
Test cases/testen!
(meten is weten)
Documenteren
(van testresultaten)
Swaptronics
Literatuur?
Berekeningen
Binnen specs?
Assumptions
(moeder van?)
Tools?
History?
Dubbele fout
Echte rootcause?
uitzoomen/pauze nemen
Oorzaak of gevolg?

## Slide 16
USS Thresher, 1963, 129 dead
USS Scorpion,1968, 99 dead
K-8:, 1970, 60 dead
K-429: 1983, 16 dead
K-219: ,1986, 6+ dead
K-278 Komsomolets: 1989, 42 dead
K-141 Kursk: 2000, 118 dead
K-159: 2003, 9 dead
List of sunken nuclear submarines
?
https://en.wikipedia.org/wiki/SUBSAFE

## Slide 17
WHY????

## Slide 18: Safety/reliability - tooling
1 pager 5 Whys 6 sigma Accelerated life testing Analysis of variance Brainstorming Cause & effects diagram (also known as fishbone or Ishikawa diagram) Control chart Correlation CTQ tree Design of experiments Failure mode and effects analysis (FMEA) Fault tree analysis Histograms | Pareto analysis Pareto chart Regression analysis Root cause analysis Run charts Scatter diagram Taguchi methods …. …. … many more….

## Slide 19
Segmentation

## Slide 28
Printing/logging
Debuggers
Pin high/low! -> oscilloscope

## Slide 30
x=3;
y=5;

## Slide 31: Test-driving development
https://en.wikipedia.org/wiki/Test-driven_development
https://www.guru99.com/test-driven-development.html

## Slide 32: SW Nasty s.... (stuff)
Memory issues?
RTOS?

## Slide 33
Rootcause analyse
A) Describe problem
B) Identify possible causes
C) Evaluate possible causes
D) Confirm true rootcause

## Slide 34
A) Describe problem
- State the problem
- Specify the problem
- What/Where/When/Extent (size)
- Is (wat is het probleem)
De I2C clock lijn crashed als de motor aan staat
- Is not (wat is niet het probleem)
Hij crashed niet als de motor separaat gevoed wordt

## Slide 35: Communicatie
Stel: een probleem wordt niet snel opgelost
EN
Er wordt niet helder over het probleem gecommuniceerd door het eigenaren team
Je baas
De baas van je baas
De klant
CLM
Career Limiting Move!

## Slide 36
Problem Statement:
Helder opgeschreven wat het probleem is (ondubbelzinnig)
Owner / Team / stakeholders:
Wie werken er aan? Wie hebben er belang in?
Success criteria:
Meetbare criteria!
SMART gedefinieerd
Current status:
Wat weten we nu al wel?
Wat is de uitkomst van testen, etc?
plans
Wanneer wordt wat gedaan?
Bv:
Test IV curve motor in wk 12
Test aan acceleratie in wk 13
1-Pager
A3
8D

## Slide 37
1-Pager
A3
8D

## Slide 38
1-Pager
A3
8D

## Slide 39
Questions?